## Slide 1: Colombia Spot Market and Interconnections
Peter Cramton
24 January 2009
Professor of Economics, University of Maryland Chairman, Market Design Inc.

## Slide 2: Interconnections
Ecuador
  Import 395 MW
  Export 535 MW
Venezuela
  Import 205 MW
  Export 336 MW
Panama
  Import 300 MW
  Export 300 MW
Total
  Import 900 MW
  Export 1171 MW

## Slide 3: Ecuador (today)
Treated like Colombia demand
  Export to Ecuador added to Colombia demand DC
  Export may raise Colombia spot price PC
Ecuador pays Ecuador spot price PE
Difference PE – PC = congestion rent
Congestion rent is split between C and E
  Colombia gets share DC/(DC+XE) (i.e., nearly 100%)
  Mostly used to subsidize Colombia demand

## Slide 4: Ecuador (future)
Treated like Colombia demand
  Export to Ecuador added to Colombia demand DC
  Export may raise Colombia spot price PC
Ecuador pays Ecuador spot price PE
Difference PE – PC = congestion rent
Congestion rent is split between C and E
  Colombia gets 50% share
  Mostly used to subsidize Colombia demand

## Slide 5: Venezuela
Venezuela agent bids import price in DA market, just like Colombia supply
For export, agent self-schedules (no bid)
Agent pays price found from marching up Colombia supply curve by amount of self-schedule
Higher Venezuela price is received by suppliers with offers between PC and PV
Venezuela export does not impact PC

## Slide 6: Problem with Venezuela solution
Use of two prices within the same zone distorts bids
  Supplies compete to get the higher clearing price
  Pushes lower price up to higher price (the true clearing price)
  Result is a distorted supply schedule that is too flat at the clearing price (for lower quantities)
    Political trick fails
    Political trick introduces inefficiencies in dispatch

## Slide 7: Interconnection proposal
Goal
  Efficient dispatch in all countries
  Optimal use of lines
  Subject to political constraints
Solution
  Use mechanism that leads to efficient dispatch
    Gather information sufficient for efficient dispatch
    Use prices that support efficient dispatch
    Use congestion rents to satisfy political constraints

## Slide 8: Efficient dispatch
Each day require supply offers from each country for a range around demand
Colombia [DC – 900, DC + 1161]
Ecuador [DE – 535, DE + 395]
Venezuela [DV – 336, DV + 205]
Panama [DP – 300, DP + 300]
Simultaneously determine efficient dispatch of all units and use of all lines

## Slide 9: Efficient dispatch and pricing
Determine prices for each of four zones PC, PV, PE, Pp that support efficient dispatch
Both suppliers and demanders in zone z are paid/pay the zonal price Pz
Price differences only exist if congestion
Price differences create congestion rents
Congestion rents can be used to handle political constraints
  Fund subsidies for poor consumers

## Slide 10: Consider other market improvements
Three-part bids
Locational marginal prices (LMP or nodal pricing)
Information policy

## Slide 11: Three-part bids for thermal units
Start-up cost
No-load cost
Marginal cost

## Slide 12: Motivation for three-part bids
Required for efficient dispatch of thermal units
  Start-up and no-load costs can be significant
  XM cannot efficiently dispatch with this information
Otherwise, generator distorts MC to account for how the bidder thinks the plant may be used
Note well: Start-up and no-load costs are only paid in the event that the generator is not breaking even (as bid) over entire day

## Slide 13: Market power with three-part bids
Only bid start-up and no-load once a month
MC only bid once a day
Only a single MC bid, rather than a schedule
Market power much more severe with 1-part bids
  Better transparency with 3-part
  Distortions required with 1-part
    Increase in MC bid (to cover start-up cost)
    Increase in Min operating level (to avoid no load loss)

## Slide 14: Locational prices
Necessary for efficient dispatch in real time
Account directly for locational differences arising from transmission constraints
If constraints are not binding, then no price differences

## Slide 15: Locational prices and market power
May be severe market power in load pockets
Addressed by constraining bids when competition is limited
  PJM’s 3-pival supplier test
    Can competitive supply less supply of three largest satisfy all demand in location?
    If not, then bids limited to cost + 10%
    Need estimate of opportunity cost for hydro unit

## Slide 16: Improved information policy
Colombia currently has full transparency
  All bid information revealed after bidding period
Allows day-by-day punishment for deviation from tacit collusion
  Much easier to support tacit collusion
Anonymous bids would be better
Then reveal all bids after 90 days
  Has benefits of full transparency
  But does not allow immediate punishment of defectors from tacit agreement